## Slide 1
SMART SHOPPING CART
PRESENTED BY
GROUP-02

## Slide 2
SCENARIO

## Slide 3
MEET THE TEAM
Punno Saha
2005002
Rafiul Islam
2005004
Farabe
2005023
Ratul joy
2005030
Nahid
2005034

## Slide 4
Introduction
Nahid
2005034
Presented By

## Slide 5
Introduction
Our Smart Shopping Cart is equipped with RFID scanning, automatic billing, a digital display, and real-time inventory tracking. It offers a user-friendly design to enhance shopping efficiency, reduce checkout time, and modernize the retail experience.

## Slide 6
Objective
.
To improve shopping by adding smart technology to the cart.
To remove the need for manual scanning or standing in checkout lines.
To make shopping easier for customers and to help stores manage giving real-time updates on products
To automatically scan and track items by connecting the cart to the store's system.

## Slide 7
Existing Product
2.Global Smart Shopping Cart Manufacturers
Red Sheep Store Fixtures (United States)
Wanzl
(Germany)
1.No Local Manufacturers in Bangladesh
Unarco Industries
(United States)
National Cart
(United States)
Technibilt
(United States)

## Slide 8
Manufacturer | Price | Features
Wanzl (Germany) | $100 - $300 | Built-in scanners Automatic billing Digital display Rechargeable battery
Unarco Industries (United States) | $75 - $250 | Built-in scanners Automatic billing Digital display 360-degree wheel rotation Rechargeable battery
Technibilt (United States) | $100 - $300 | Built-in scanners,Automatic billing Digital display Rechargeable battery,Phone charging, Touch screen
National Cart (United States) | $50 | Built-in scanners Automatic billing
RedSheep Store Fixtures (United States) | $75 - $150 | Built-in scanners Rechargeable battery Digital display Task screen
Competitor Analysis:

## Slide 9
MARKET ANALYSIS
Survey
Consumer Survey
Shop Owner Survey

## Slide 10
Easy Connection
User-Friendly Design
Business Idea
NEED
STATEMENT
To meet the needs of shoppers and store owners, we should follow these guidelines
Affordable Price
Real-Time Tracking
Strong and Light
User- Friendly Design

## Slide 11
60%
30%
10%
Large and Medium Supermarkets
Wholesale Retailers and Big Stores
New Retail Stores in Cities
TARGET CUSTOMER

## Slide 12
Rafiul Islam
2005004
Data Analysis
Objective Tree, Kano Model, Function Tree, Function Tree Diagram
Presented By

## Slide 13
Variety Of
Products
Well Organized
And Easy To
Find Products
No Bargaining
Near Home
Or Work Place
60
40
20
0
54%
46%
Male
Female
Reasons for selecting supermarkets for shopping
Gender distribution of people going supershops for shopping

## Slide 14
Disagree
Agree
Highly Agree
Highly Disagree
60
40
20
0
70
Counts what people think that standing in line and scanning each product code is a waste of time
Age range of people go to super shops for shopping
51 years up
26-35 years
18-25 years
36-50 years
28.2%
6.5%
7.3%
58.1%

## Slide 15
0
Dissatisfied
Satisfied
Neutral
Very Satisfied
10
20
30
40
50
Satisfaction levels of consumers on current shopping experiences
Percentage of people think that it is time consuming to pay the bill in departmental shops after standing in line to scan each product
Yes
88.8%
No
11.2%

## Slide 16
71.2%
28.8%
Automatic Billing With Payment
Automatic Billing Only
Businessman
Service Holder
Engineer
Student
Doctor
Teacher
Housewife
30
20
10
0
Different professions of people go to super shops
Counts what features consumers find most useful in a smart cart?

## Slide 17
KANO MODEL
Discrete Analysis |  |  |  |  |  |  | 
Feature Name | M | O | A | I | R | Q | Evaluation
Built in scanner | 53.60% | 12.00% | 6.40% | 23.20% | 3.20% | 1.60% | Must Be
Wheel rotation of 360 degree | 48.80% | 10.40% | 7.20% | 28.00% | 4.80% | 0.80% | Must Be
Automatic billing with payment | 42.40% | 16.00% | 8.00% | 31.20% | 0.80% | 1.60% | Must Be
Digital display | 16.00% | 13.60% | 36.80% | 27.20% | 4.00% | 2.40% | Indifferent

## Slide 18
KANO MODEL
Continuous Analysis |  |  | 
Feature Name | Disfunctional (X) | Functional(Y) | Category
Built in Scanner | 2.8 | 0.256 | Must Be
Wheel rotation of 360 degree | 2.552 | 0.048 | Must Be
Automatic billing with payment | 2.744 | -0.024 | Must Be
Digital display | 1.528 | -1.736 | Indifferent
X-axis | Y-axis
2 | -1

## Slide 19
OBJECTIVE TREE
Enhance The Shopping Experiences In Bangladesh
Increase Efficiency
Improve
Customer
Satisfaction
Optimize Store Operations
Enhance Data Collection and Analysis
Reduce checkout time
Streamline the billing process
Provide real-time billing information
Offer Personalized product recommendations
Automate inventory management
Reduced manpower required for billing
Analyze sales trends for better stock
Gather customer shopping behaviour data

## Slide 20
Smart Shopping Cart
User
Input
Purchasing
Through
Automated Billing
Black Box
In product design, black box refers to a component or system whose internal workings are not transparent or visible to the user or the outside observer.
Fig : Black box diagram

## Slide 21
Customer
Action
(Scanning)
Sensor
(Product
Detection)
Control
Unit
IoT Data
Transmission
Stored
Product
Data
Display
Billing Info
Customer
Interaction
(Payment)
Function Tree

## Slide 22
Arduino
Connect to the shop server
RFID Reader
RFID Tag Scanning
Product Detection
IoT Data
Transmission
Data Processing
Digital Billing Info
Online Payment
User Input
Wi-Fi
Power
Micro Controller
Functional Structure Diagram

## Slide 23
Farabe
2005023
QFD, Specification & Design Analysis
Presented By

## Slide 24
QUALITY FUNCTION
DEPLOYMENT (QFD)
Type of correlation | Symbols
Strongly Positive | ++
Positive | +
No correlation | 
Negative | -
Strongly Negative | --
Type of relation | Symbol | Value
No relation |  | 0
Weak relation | ▽ | 1
Moderate relation | □ | 3
Strong relation |  | 9
Improvement | Direction
Increase | ▲
Decrease | ▼

## Slide 25
DIFFERENT TYPES OF MATRIX IN QFD

## Slide 27
Priority Level | Technical Aspect | Weight (%)
High | Material Quality (Objective) | 10
High | RFID Technology for Monitoring & Item Scanning | 9
High | Inventory Management | 9
Medium | Weight (Subjective) | 8
Medium | Production Cost | 8
Medium | API Integration | 8
Medium | 10hr Battery Life | 8
Low | Touchscreen Interface | 6
Low | Wi Fi Modules | 6
Low | GPS | 6
Low | Real Time Promotions | 6
Low | Multi-language Support | 5
Low | Modification (Subjective) | 5
Low | Dimension (mm) | 5
Low | 12V 7.5Ah Battery | 5
FINDINGS OF QFD

## Slide 28
Insert title here
Lorem Ipsum is simply dummy text of the printing and typesetting is simply dummy text
Insert title here
Lorem Ipsum is simply dummy text of the printing and typesetting is simply dummy text
Insert title here
Lorem Ipsum is simply dummy text of the printing and typesetting is simply dummy text
SPECIFICATION CHART
Type | Component | Specification | Quantity
Electronic | Arduino Nano | Main controller, compact size, low cost, 5V operation | 1
Electronic | 20x4 LCD Display with I2C | 5V operation, connected via I2C (SCL, SDA, VCC, GND) | 1
Electronic | SIM800L GSM Module | GSM communication, connected via UART (D2, D3 pins), low power consumption | 1
Electronic | EM-18 Module Reader | RFID technology, operating at 125 kHz, connected to 5V DC supply | 1
Electronic | EM-18 Tag | RFID tags compatible with EM-18 module | 4
Electronic | Push Button | Standard button, triggers actions such as item removal and SMS sending | 2
Electronic | Red LED | Indicator LED, connected for status display | 1
Electronic | Green LED | Indicator LED, connected for status display | 1
Electronic | Buzzer | Provides audible feedback for certain actions | 1
Electrical | 12V 7.5A Li-Ion Battery | Power source for the system, 3.7V rechargeable battery | 1
ELECTRICAL COMPONENTS

## Slide 29
Insert title here
Lorem Ipsum is simply dummy text of the printing and typesetting is simply dummy text
Insert title here
Lorem Ipsum is simply dummy text of the printing and typesetting is simply dummy text
Insert title here
Lorem Ipsum is simply dummy text of the printing and typesetting is simply dummy text
Type | Component | Specification | Quantity
Mechanical | Shopping Cart Frame | Cast alloy steel, designed for durability and load-bearing | 1
Mechanical | Wheels | 360-degree rotating wheels for smooth mobility | 4
Mechanical | Load-Bearing Structure | Supports up to 240 kg of load | 1
Mechanical | Battery Holder | Compartment designed to fit a 3.7V Li-ion battery | 1
Mechanical | Mounting Brackets | For securing the LCD display, GSM module, and other electrical components | Multiple
Mechanical | Protective Enclosure Box | Houses and protects all electrical components from damage | 1
Mechanical | Phone holder | For holding the phone during shopping | 1
Mechanical | Basket | where users can place their items. | 1
MECHANICAL COMPONENTS

## Slide 30
ELECTRICAL
MAIN
COMPONENTS
Arduino Nano
20x4 LCD Display with I2C
EM-18 RFID Module Reader

## Slide 31
MECHANICAL
ELECTRICAL
MAIN
COMPONENTS
Frame Structure
Cart Basket
Wheels

## Slide 35
Stress
Analysis
Name | Type | Min | Max
Stress1 | VON: von Mises Stress | 0.000e+00N/m^2 Node: 1097 | 1.207e+08N/m^2 Node: 49448

## Slide 36
Name | Type | Min | Max
Stress1 | VON: von Mises Stress | 0.000e+00N/m^2 Node: 1097 | 1.207e+08N/m^2 Node: 49448
Strain
Analysis

## Slide 37
Name | Type | Min | Max
Factor of Safety2 | Automatic | 1.999e+00 Node: 49448 | 1.000e+16 Node: 1097
Factor of
Safety

## Slide 38
Thermal Analysis

## Slide 39
Simulation Data table
Load (N) | Max Stress (N/m²) | Max Displacement (mm) | Factor of Safety (FOS)
1080 | 120700000 | 6.741 | 2
1181.052632 | 330889473.7 | 7.357421053 | 1.916126316
1282.105263 | 541078947.4 | 7.973842105 | 1.832252632
1383.157895 | 751268421.1 | 8.590263158 | 1.748378947
1484.210526 | 961457894.7 | 9.206684211 | 1.664505263
1585.263158 | 1171647368 | 9.823105263 | 1.580631579
1686.315789 | 1381836842 | 10.43952632 | 1.496757895
1787.368421 | 1592026316 | 11.05594737 | 1.412884211
1888.421053 | 1802215789 | 11.67236842 | 1.329010526
1989.473684 | 2012405263 | 12.28878947 | 1.245136842
2090.526316 | 2222594737 | 12.90521053 | 1.161263158
2191.578947 | 2432784211 | 13.52163158 | 1.077389474
2292.631579 | 2642973684 | 14.13805263 | 0.993515789
2393.684211 | 2853163158 | 14.75447368 | 0.909642105
2494.736842 | 3063352632 | 15.37089474 | 0.825768421
2595.789474 | 3273542105 | 15.98731579 | 0.741894737
2696.842105 | 3483731579 | 16.60373684 | 0.658021053
2797.894737 | 3693921053 | 17.22015789 | 0.574147368
2898.947368 | 3904110526 | 17.83657895 | 0.490273684
3000 | 4114300000 | 18.453 | 0.4064

## Slide 40
Different types of Graphs

## Slide 42
Punno Saha
2005002
Material Selection &
Manufacturing Process
Presented by

## Slide 43
Material Selection
The main goal of material selection is to minimize cost while meeting product performance goals. The cost and properties of candidate materials begin the process of material selection.

## Slide 44
We use the Digital Logic Method to select the material of our product. In the Digital Logic Method, we find the value of α and β in the following way. The performance index, Y= Σαβ and the material with the highest value of ϒ is considered the best.

## Slide 45
Material Selection of Cart’s Frame
Selection Criteria |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Positive Decisions | Relative Emphasis Co- efficient
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 |  | 
1.Ultimate Strength | 1 | 1 | 1 | 1 | 1 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 6 | 0.28
2. Toughness | 0 |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 |  |  |  |  |  |  |  |  |  |  | 5 | 0.24
3. Cost |  | 0 |  |  |  |  | 0 |  |  |  |  | 1 | 0 | 1 | 1 |  |  |  |  |  |  | 3 | 0.14
4.Rust Corrosion |  |  | 0 |  |  |  |  | 0 |  |  |  | 0 |  |  |  | 1 | 1 | 0 |  |  |  | 2 | 0.09
5.Electrical Conductivity |  |  |  | 0 |  |  |  |  | 0 |  |  |  | 1 |  |  | 0 |  |  | 0 | 0 |  | 1 | 0.05
6.Weight |  |  |  |  | 0 |  |  |  |  | 0 |  |  |  | 0 |  |  | 0 |  | 1 |  | 0 | 1 | 0.05
7.Young's Modulus |  |  |  |  |  | 0 |  |  |  |  | 0 |  |  |  | 0 |  |  | 1 |  | 1 | 1 | 3 | 0.14

## Slide 46
Table: Properties of Candidate material for frame
Material Properties |  |  |  |  | Minimum Value Required | Maximum Value Required
 | Mild Steel (Coated) | Aluminum (Standard Grades) | Stainless Steel (Grade 304) | HighStrength Low-Alloy (HSLA) Steel |  | 
1. Ultimate Strength (MPa) | 450 | 200 | 600 | 850 | 200 | 850
2. Toughness(J) | 150 J | 80 J | 200 J | 250 J | 80 | 250
3. Cost/kg (Tk) | 90 | 270 | 400 | 155 | 90 | 400
4.Rust Corrosion (mm/year) | 0.2 | 0.015 | 0.005 | 0.08 | 0.005 | 0.2
5. Electrical Conductivity (MS/m) | 6.99 | 37.7 | 1.45 | 4.5 | 1.45 | 37.7
6. Weight/m3 | 7850 | 2700 | 8000 | 7800 | 2700 | 8000
7.Youngs Modulus | 210 | 70 | 193 | 205 | 70 | 210

## Slide 47
Table: Scaled values of properties and performance Index of Carts Frame
 |  | Mild Steel (Coated) |  | Aluminum (Standard Grades) |  | Stainless Steel (Grade 304) |  | High-Strength Low- Alloy (HSLA) Steel | 
Selection Criteria | Weighting Factor (α) | Scale Property, (β) | Weighted Score, (αβ) | Scale Property (β) | Weighted Score (αβ) | Scale Property (β) | Weighted Score αβ | Scale Property (β) | Weighted Score (αβ)
1. Ultimate Strength (MPa) | 0.28 | 52.94 | 14.82 | 23.53 | 6.59 | 70.59 | 19.76 | 100 | 28
2. Toughness(j) | 0.24 | 60 | 14.4 | 32 | 7.68 | 80 | 19.2 | 100 | 24
3. Cost/kg (Tk) | 0.14 | 100 | 14 | 33.33 | 4.67 | 33.33 | 4.67 | 50.06 | 7.01
4.Rust Corrosion(mm/y ear) | 0.09 | 2.5 | 0.23 | 33.33 | 2.99 | 100 | 9 | 6.25 | 0.56
5. Electrical Conductivity (MS/m) | 0.05 | 20.74 | 1.04 | 3.85 | 0.19 | 100 | 5 | 32.22 | 1.61
6. Weight/m3 | 0.05 | 34.39 | 1.72 | 100 | 5 | 33.75 | 1.69 | 34.62 | 1.73
7. Young’s Modulus | 0.14 | 100 | 14 | 33.33 | 4.67 | 91.9 | 12.87 | 97.62 | 13.67
 |  |  | 𝛴αβ =60.21 |  | 𝛴αβ =31.79 |  | 𝛴αβ =72.19 |  | 𝛴αβ =76.58

## Slide 48
Result & Analysis
From the value of ϒ= 𝛴αβ = 76.58 , we can see that High strength low alloy steel (HSLA) has the highest value of the performance index. So, High strength low alloy steel (HSLA) selected for the carts frame and cage.

## Slide 49
Selection criteria | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | Positive decisions | Relative importance coefficient (α)
Material Strength & Compatibility | 1 | 0 | 1 | 0 |  |  |  |  |  |  | 2 | 0.2
Surface finish | 0 |  |  |  | 1 | 0 | 0 |  |  |  | 1 | 0.1
Manufacturing Cost & Scalability |  | 1 |  |  | 0 |  |  | 0 | 0 |  | 1 | 0.1
Integration of Electronics & Wiring Management |  |  | 0 |  |  | 1 |  | 1 |  | 0 | 2 | 0.2
Structural Strength & Load-Bearing Capacity |  |  |  | 1 |  |  | 1 |  | 1 | 1 | 4 | 0.4
 |  |  |  |  |  |  |  |  |  |  | ∑ (Positive Decision) =10 | 1
Table - Relative importance of Selection Criterion
Manufacturing Process:
Production Cost
Structural Strength
Surface Finish

## Slide 50
 | Manufacturing Process |  | 
Properties | Casting and machining | Metal Forming and welding | Welding and Assembly Process
Manufacturing Cost & Scalability (taka) | 3225 | 3875 | 3670
Surface finish (μm) | 3.2 | 6.3 | 3.2
Integration of Electronics & Wiring Management | 0.4 | 0.25 | 0.3
Material Strength & Compatibility (Mpa) | 280 | 240 | 320
Material Compatibility | 8 | 6.5 | 9
Table - Properties
Selection criteria | Relative importance coefficient(α)
Material Strength & Compatibility | 0.2
Surface finish | 0.2
Manufacturing Cost & Scalability | 0.1
Integration of Electronics & Wiring Management | 0.1
Material Compatibility | 0.4
Performance Index (g) | 
Table - Chart for relative evaluation

## Slide 51
Selection criteria | Relative importance coefficient (α) | Casting and machining | 
 |  | Scaled Property, β | Weighted Score, αβ
Material Strength & Compatibility | 0.2 | 120.1550388 | 24.03100775
Surface finish | 0.2 | 100 | 20
Manufacturing Cost & Scalability | 0.1 | 160 | 16
Integration of Electronics & Wiring Management | 0.1 | 116.6666667 | 11.66666667
Material Compatibility | 0.4 | 123.0769231 | 49.23076923
Performance Index (g) |  |  | 120.9284436
Metal Forming and welding |  | welding and Assembly Process | 
Scaled Property, β | Weighted Score, αβ | Scaled Property, β | Weighted Score, αβ
83.22580645 | 16.64516129 | 105.5858311 | 21.11716621
50.79365079 | 10.15873016 | 100 | 20
100 | 10 | 120 | 12
100 | 10 | 133.3333333 | 13.33333333
100 | 40 | 138.4615385 | 55.38461538
 | 86.80389145 |  | 121.8351149
Table- Determination of Performance Index of manufacturing Processes

## Slide 52
Welding and Assembly Process

## Slide 53
Ratul joy
2005030
Cost Analysis

## Slide 54
Cost Analysis
Fixed Cost
Variable Cost
BOM

## Slide 55
Bill of Material (BOM)
Table: BOM of Smart Shopping Cart (For Mass Production)
Components | Quantity | Material | Unit Cost (BDT) | Total Cost (BDT) | % of Cost
Frame (Cart Structure) | 1 | High-strength low-alloy steel | 3,000 | 3,000 | 20%
Wheels | 4 | Rubber | 300 | 1,200 | 8%
Basket | 1 | Steel | 1,500 | 1,500 | 10%
Display Screen | 1 | LCD/LED | 2,500 | 2,500 | 17%
RFID Scanner | 1 | Plastic/Metal | 1,200 | 1,200 | 8%
Arduino Nano | 1 | Electronic Components | 400 | 400 | 3%
Electrical Box | 1 | Plastic | 600 | 600 | 4%
EM18 | 1 | Electronic Components | 800 | 800 | 5%
Battery | 1 | Lithium-ion/Lead Acid | 2,000 | 2,000 | 13%
Total |  |  |  | 13,100 | 100%

## Slide 56
Life Cycle Cost
We have estimated that the lifecycle of our product is 5 years.

## Slide 57
Table: Life Cycle Cost of Smart Shopping Cart
Fixed Cost (BDT) | 1st Year | 2nd Year | 3rd Year | 4th Year | 5th Year | Lifecycle | Variable Cost (BDT)
R&D |  |  |  |  |  |  | 
Design | 34955 | 0 | 0 | 0 | 0 | 34955 | 
Improvements | 4255 | 4255 | 4255 | 4255 | 4255 | 21275 | 
Total R&D Cost | 39210 | 4255 | 4255 | 4255 | 4255 | 50000 | 
Facilities |  |  |  |  |  |  | 
Land |  |  |  |  |  | 6000000 | 
Depreciation | 67050 | 67050 | 67050 | 67050 | 67050 | 335250 | 
Total Facilities Expense | 67050 | 67050 | 67050 | 67050 | 67050 | 6335250 | 
Production |  |  |  |  |  |  | 
BOM |  |  |  |  |  |  | 13,705
Labour cost |  |  |  |  |  |  | 350
Maintenance | 56275 | 60780 | 74900 | 85060 | 95505 | 372520 | 
Utilities | 250000 | 350000 | 420000 | 500000 | 460000 | 1980000 | 
Insurance | 500000 | 50000 | 50000 | 50000 | 50000 | 250000 | 
Total Production Cost | 806275 | 460780 | 544900 | 635060 | 605505 | 2602520 | 

## Slide 58
Table: Life Cycle Cost of Smart Shopping Cart
Marketing |  |  |  |  |  | 
Awareness | 120000 | 100000 | 80000 | 60000 | 40000 | 400000
Accessibility | 66980 | 70550 | 77080 | 87950 | 99575 | 402135
Total Marketing Cost | 186980 | 170550 | 157080 | 147950 | 139575 | 802135
Distribution |  |  |  |  |  | 
Logistics | 56750 | 67850 | 74320 | 81235 | 90505 | 370660
Avg. Shipping | 25000 | 25000 | 25000 | 25000 | 25000 | 125000
Total Distribution Cost | 81750 | 92850 | 99320 | 106235 | 115505 | 495660
Customer Service |  |  |  |  |  | 
Free 1st Month Adjustment | 5275 | 6200 | 6975 | 7505 | 5000 | 30955
Total Customer Service Cost | 5275 | 6200 | 6975 | 7505 | 5000 | 30955

## Slide 59
Table: Life Cycle Cost of Smart Shopping Cart
Additional Overheads |  |  |  |  |  |  | 
Administrative | 378755 | 425075 | 478655 | 500050 | 529875 | 2312410 | 
Patent | 50000 |  |  |  |  | 50000 | 
Lawsuits | 20000 | 20000 | 20000 | 20000 | 20000 | 100000 | 
Software License | 2000 | 2000 | 2000 | 2000 | 2000 | 10000 | 
Total Overhead Costs | 450755 | 447075 | 500655 | 522050 | 551875 | 2472410 | 
End of Life Cycle Project |  |  |  |  |  |  | 
Decommissioning |  |  |  | 50777 | 57560 |  | 
Waste Management |  |  |  | 30670 | 32887 |  | 
Total EOC Cost |  |  |  | 81447 | 90447 |  | 
Total Accumulated Cost | 1637295 | 1248760 | 1380235 | 1490105 | 1488765 | 12788930 | 14,055

## Slide 60
Sales Scenario
Year | Sales (Unit)
1 | 350
2 | 526
3 | 875
4 | 822
5 | 650
Total unit produced | 3223

## Slide 61
Cost Calculation
• Variable Cost: 1. Bill of Materials: Total per unit cost = 13705 Taka . Lifecycle Cost: Total accumulated variable cost = 13705*3223= 44171215 Taka
• Fixed Cost:
1. Lifecycle Cost: Total accumulated fixed cost = 12788930 Taka
• Total Cost: Fixed Cost + Variable Cost = 56960145 Taka.
• Per Unit Cost:
𝑇𝑜𝑡𝑎𝑙 𝐶𝑜𝑠𝑡 ÷ 𝑇𝑜𝑡𝑎𝑙 𝑈𝑛𝑖𝑡 𝑃𝑟𝑜𝑑𝑢𝑐𝑒𝑑 = 56960145/3223 = 17673 Taka

## Slide 62
Let, BEPx = Break Even Point in Units.
BEP$ = Break Even Point in Takas.
S = Selling price per unit = 20000 Taka
Q = Total number of units produced = 3223
TR = Total Revenue = (𝑠 × 𝑄) = Total Sales = 64460000 Taka
F = Fixed Cost = 12788930 Taka V = Variable Cost = 13705 Taka
TC = Total Cost = F + VQ = 56960145 Taka
Break Even Point occurs when TR = TC
𝑩𝑬𝑷𝒙 = 𝑭/(S-V) =12788930/(20000-13705) = 2032 Units.
𝑩𝑬𝑷$ = 𝑩𝑬𝑷𝒙 × 𝑺 = 2032*20000 = 40640000 Taka.
𝑷𝒓𝒐𝒇𝒊𝒕 = 𝑻𝑹 - 𝑻𝑪 =64460000-56960145 = 7499855 Taka.
64460000 Taka
Total Revenue
Total Cost
56960145 Taka
Break Even
Analysis

## Slide 63
Break-Even Graph

## Slide 64
Our Prototype

## Slide 65
Conclusion
Smart Shopping Cart enhances efficiency in retail shopping.
Features include RFID scanning, automatic billing, and digital display.
Designed based on extensive market and consumer analysis.
Stress and thermal analysis confirm structural strength and safety.
Locally developed to reduce reliance on imports.
Cost-effective design within 10,000–12,000 BDT.
High market potential in Bangladesh’s modern retail sector.
Validated using QFD, function structure, and simulation tools.
Suitable for mass production using stamping and welding processes.
Powered by durable battery with safe electronic integration.

## Slide 66
THANK YOU